## Slide 1: Ophthalmic diagnostic tools
Tools &Instrument &drugs
By dr. Eman Enweigi

## Slide 2: Snellen chart:
an eye chart that can be used to measure visual acuity
the standard chart distance is 6 metres (20 ft), and normal acuity is designated "6/6

## Slide 4: Retinoscopy
a technique to obtain an objective measurement of the refractive error of a patient's eyes Manually.
The examiner uses a retinoscope to shine light into the patient's eye and observes the reflection (reflex) off the patient's retina.
While moving the streak or spot of light across the pupil the examiner observes the relative movement of the reflex and manually places lenses over the eye (using a trial frame and trial lenses) to "neutralize" the reflex.

## Slide 5
Retinoscope
objective measurement of the refractive error of a patient's eyes Manually.

## Slide 6
Retinoscopy

## Slide 7
Myopes display an "against" reflex
Hyperopes, on the other hand, display a "with" movement

## Slide 8: Auto refractometer
a computer-controlled machine used during an eye examination to provide an objective measurement of a person's refractive error and prescription for glasses or contact lenses.

## Slide 10: Trial Box
Uses:
Objective Refraction
Subjective Refraction
Diagnosis Of Squint

## Slide 11
Trial lens
Minus spherical for myopia correction
Plus spherical for hypermeteropia correction
Minus cylinder for myopic stigmatism
Plus cylinder for hpermateropic stigmatism

## Slide 12: TRIAL FRAME
eyeglass frame designed to permit insertion of different lenses used in correcting refractive errors

## Slide 14: Occluder
It is an opaque plastic disc to Occlude one eye
Used to dissociate fusion
Used to close one eye while the other eye can be tested for visual acuity

## Slide 15: Pin Hole Disc
Opaque disc with pinhole of 1-2 mm diameter in its centre.
To find out if the loss of vision is due to an error of refraction or some organic lesion

## Slide 16
Douchrome Test:
a test commonly used to refine the final sphere in refraction, which makes use of the chromatic aberration of the eye.
Because of the chromatic aberration of the eye, the shorter wavelengths (green) are focused in front of the longer red wavelengths

## Slide 18
Color Vision Testing
performed using Ishihara polychromatic plates

## Slide 19: Amsler Grid
Amsler grid evaluate central 20 degree of visual field
Mainly for macular diseases screening and monitoring

## Slide 22: Slit Lamp biomicroscope

## Slide 23
Siltlamp with +90 +78 +60 For fundoscopy

## Slide 24: Slit Lamp Biomicriscopy With Contact Goldman 3 Mirror Lens for fundus examination

## Slide 25: Goldmann’s Applanation tonometer: for the measurement of IOP
Fluorescein rings

## Slide 26
Ophthalmoscope:

## Slide 28
Optical coherence tomography (OCT)
is a non-invasive imaging test.
uses light waves to take cross-section pictures of retinal layers .

## Slide 30
Fluorescein Angiography
It is an invasive procedure in which fluorescein dye is injected, usually into an antecubital vein.
Within 10 to 15 seconds, this dye can be seen coursing through the retinal vessels.
Over a 10-minute period, serial black-and-white photographs are taken of the retinal vasculature

## Slide 32
Fluroscene angiography photo
Red free fundus photo

## Slide 33: Perimeter:
Perimetry (visual field test )
For assessment of visual field loss

## Slide 34: Corneal topography
is a computer assisted diagnostic tool that creates a three-dimensional map of the surface curvature of the cornea

## Slide 35
Topographical map of the cornea
Blue color represent flat areas
Red represent steeper cornea

## Slide 36: Diagnostic agents
Topical anesthesia
Tonometry (measurement of intraocular pressure)
removal of corneal foreign bodies,
removal of sutures
Gonioscopy , triple mirror

## Slide 37: Fluorescein dye
Uses
Corneal epithelial defects & corneal ulcers.
Intraocular pressure measurement
Seidel's test: Concentrated fluorescein dye
Jones dye test for assessment of lacrimal passage functional potency
Tear film break up time(TBUT) dry eye

## Slide 39
Rose bengal is actually a derivative of fluorescein
Stains the devitalized cells only
It aids in evaluation of
Keratoconjunctivitis sicca
Corneal defects . Dendritic ulcers

## Slide 40: Cycloplegic &mydriatic

## Slide 43
Thank you