## Slide 1: ECG
Dr. Zaki Bettamer,MD
Zikoecho @yahoo.com

## Slide 6: ECG leads
• To ascertain the direction of a wavefront, the
ECG is recorded from different sites called lead
Recording 12 lead ECG:
• 6 horizontal bipolar leads( I,II, III, aVR, aVL,
aVF).
• 6 frontal leads unipolar leads(V1 – V6).

## Slide 9: The vertical plane - the six limb leads
-
-
-
+
+
+
Lead I
Lead II
Lead III
Lead aVR
Lead aVL
Lead aVF
+
+
-
-
-
-
+
-
-
7.4
Notes: The vertical plane - the six limb leads
The three electrodes are placed on the right (R) and left arms (L) and the left leg (F) with the neutral lead on the right leg, usually on the wrists and ankles.
Lead I is obtained by connecting L to the positive terminal and R to the negative terminal.
Lead II records with the left leg connected to the positive and the right arm to the negative.
Lead III records with the left foot connected to the positive and the left arm to the negative.
aVR, aVL, and aVF are considered to look at the heart from the right arm, left arm and left leg.
Leads I and aVL give most information about the lateral border, leads II, III, and aVF obtain most information about the inferior (or posterior) and the precordial leads give information about the anterior aspect of the heart.

## Slide 10: Horizontal plane - the six chest leads
7.5
RA
LA
LV
RV
V1
V1
V2
V2
V3
V3
V4
V4
V5
V5
V6
V6
Notes: Horizontal plane - the six chest leads
Each of the six chest leads has a fixed position. In order to place the precordial leads correctly the fourth intercostal space needs to be identified. The ribs form convenient horizontal landmarks. In order to count them, feel for the ridge with marks the junction of the manubrium and the body of the sternum. When this has been found, run the finger outwards until it reaches the second costal cartilage, which articulates with the sternum at this level. The space immediately above this is the first intercostal space. The spaces should then be counted downwards, well away from the sternum, as they are more easily felt here.
V1 right sternal margin at fourth intercostal space
V2 left sternal margin at fourth intercostal space
V3 midway between V2 and V4
V4 intersection of left midclavicular line and fifth intercostal space
V5 intersection of left anterior axillary line with a horizontal line through V4
V6 intersection of mid-axillary line with a horizontal line through V4 and V5.
V1 and V2 face and lie close to the free wall of the right ventricle, V3 and V4 lie near to the interventricular septum with V4 usually at the cardiac apex, and V5 and V6 face the free wall of the left ventricle but are separated from it by a substantial distance.
Together the chest leads observe changes in the anterior and lateral aspects of the heart, giving detailed information about the myocardium of the area they lie over.

## Slide 12: RT sided ECG.

## Slide 15
Reading normal ECG

## Slide 16: Normal Impulse Conduction
Sinoatrial node
AV node
Bundle of His
Bundle Branches
Purkinje fibers

## Slide 17: Impulse Conduction & the ECG
Sinoatrial node
AV node
Bundle of His
Bundle Branches
Purkinje fibers

## Slide 18: The “PQRST”
P wave - Atrial depolarization
T wave - Ventricular repolarization
QRS - Ventricular depolarization

## Slide 19: The PR Interval
Atrial depolarization
+
delay in AV junction
(AV node/Bundle of His)
(delay allows time for the atria to contract before the ventricles contract)

## Slide 20: Anatomy of Heart and ECG signal

## Slide 21: Pacemakers of the Heart
SA Node - Dominant pacemaker with an intrinsic rate of 60 - 100 beats/minute.
AV Node - Back-up pacemaker with an intrinsic rate of 40 - 60 beats/minute.
Ventricular cells - Back-up pacemaker with an intrinsic rate of 20 - 45 bpm.

## Slide 22: The ECG Paper
Horizontally
  One small box - 0.04 s
  One large box - 0.20 s
Vertically
  One large box - 0.5 mV

## Slide 24: The ECG Complex with Interval and Segment Measurements

## Slide 25: Remember This 3, 3, 3 and 5
P duration = 3 small sqs = 0.12 sec.
P height = 3 small sqs = 0.12 sec.
QRS duration = 3 small sq = 0.12 sec.
P-R interval = 5 small sqs = 0.2 sec.

## Slide 26: ECG Paper and related Heart Rate & Voltage Computations

## Slide 28: Rhythm Analysis
Step 1: Calculate rate.
Step 2: Determine regularity.
Step 3: Assess the P waves.
Step 4: Determine PR interval.
Step 5: Determine QRS duration.

## Slide 29: The ECG Paper (cont)
Every 3 seconds (15 large boxes) is marked by a vertical line.
This helps when calculating the heart rate.
3 sec
3 sec

## Slide 30: Step 1: Calculate Rate
Option 1
  Count the # of R waves in a 6 second rhythm strip, then multiply by 10.
Interpretation?
9 x 10 = 90 bpm
3 sec
3 sec

## Slide 31: Step 1: Calculate Rate
Option 2 (cont)
  Memorize the sequence:
  300 - 150 - 100 - 75 - 60 - 50
Interpretation?
300
150
100
75
60
50
  Approx. 1 box less than 100 = 95 bpm

## Slide 32: Rate:
If regular : Divide 300/ number of large squares between 2 Rs = HR
If irregular: Count number of complexes in 6 sec. and multiply by 10
RATE may be: P = Sinus
Normal 60 -100 No P = Non sinus
Bradycardia < 60
Tachycardia > 100

## Slide 33: Step 2: Determine regularity
Look at the R-R distances (using a caliper or markings on a pen or paper).
Regular (are they equidistant apart)? Occasionally irregular? Regularly irregular? Irregularly irregular?
Interpretation?
Regular
R
R

## Slide 34: Step 3: Assess the P waves
Are there P waves?
Do the P waves all look alike?
Do the P waves occur at a regular rate?
Is there one P wave before each QRS?
Interpretation?
Normal P waves with 1 P wave for every QRS

## Slide 35: Step 4: Determine PR interval
Normal: 0.12 - 0.20 seconds.
(3 - 5 boxes)
Interpretation?
0.12 seconds

## Slide 36: Step 5: QRS duration
Normal: 0.04 - 0.12 seconds.
(1 - 3 boxes)
Interpretation?
0.08 seconds

## Slide 37: Rhythm Summary
Rate 90-95 bpm
Regularity regular
P waves normal
PR interval 0.12 s
QRS duration 0.08 s
Interpretation?
Normal Sinus Rhythm

## Slide 38: NSR Parameters
Rate 60 - 100 bpm
Regularity regular
P waves normal
PR interval 0.12 - 0.20 s
QRS duration 0.04 - 0.12 s
Any deviation from above is sinus tachycardia, sinus bradycardia or an arrhythmia

## Slide 39: The QRS Axis
The QRS axis represents the net overall direction of the heart’s electrical activity.
Abnormalities of axis can hint at:
Ventricular enlargement
Conduction blocks (i.e. hemiblocks)

## Slide 40: Determining the Axis
Predominantly Positive
Predominantly Negative
Equiphasic

## Slide 41: The Quadrant Approach
1. Examine the QRS complex in leads I and aVF to determine if they are predominantly positive or predominantly negative. The combination should place the axis into one of the 4 quadrants below.

## Slide 42: Quadrant Approach: Example 1
Negative in I, positive in aVF  RAD
The Alan E. Lindsay ECG Learning Center http://medstat.med.utah.edu/kw/ecg/

## Slide 43
30 bpm
Rate?
Regularity?
regular
normal
0.10 s
P waves?
PR interval?
0.12 s
QRS duration?
Interpretation?
Sinus Bradycardia

## Slide 44: Sinus Bradycardia
Deviation from NSR
- Rate < 60 bpm

## Slide 45
130 bpm
Rate?
Regularity?
regular
normal
0.08 s
P waves?
PR interval?
0.16 s
QRS duration?
Interpretation?
Sinus Tachycardia

## Slide 46: Sinus Tachycardia
Deviation from NSR
- Rate > 100 bpm

## Slide 47
70 bpm
Rate?
Regularity?
occasionally irreg.
2/7 different contour
0.08 s
P waves?
PR interval?
0.14 s (except 2/7)
QRS duration?
Interpretation?
NSR with Premature Atrial Contractions

## Slide 48
60 bpm
Rate?
Regularity?
occasionally irreg.
none for 7th QRS
0.08 s (7th wide)
P waves?
PR interval?
0.14 s
QRS duration?
Interpretation?
Sinus Rhythm with 1 PVC

## Slide 49: Teaching Moment
When an impulse originates in a ventricle, conduction through the ventricles will be inefficient and the QRS will be wide and bizarre.

## Slide 50
100 bpm
Rate?
Regularity?
irregularly irregular
none
0.06 s
P waves?
PR interval?
none
QRS duration?
Interpretation?
Atrial Fibrillation

## Slide 51
70 bpm
Rate?
Regularity?
regular
flutter waves
0.06 s
P waves?
PR interval?
none
QRS duration?
Interpretation?
Atrial Flutter

## Slide 52
74 148 bpm
Rate?
Regularity?
Regular  regular
Normal  none
0.08 s
P waves?
PR interval?
0.16 s  none
QRS duration?
Interpretation?
Paroxysmal Supraventricular Tachycardia (PSVT)

## Slide 53
160 bpm
Rate?
Regularity?
regular
none
wide (> 0.12 sec)
P waves?
PR interval?
none
QRS duration?
Interpretation?
Ventricular Tachycardia

## Slide 54
none
Rate?
Regularity?
irregularly irreg.
none
wide, if recognizable
P waves?
PR interval?
none
QRS duration?
Interpretation?
Ventricular Fibrillation

## Slide 55: AV Nodal Blocks
1st Degree AV Block
2nd Degree AV Block, Type I
2nd Degree AV Block, Type II
3rd Degree AV Block

## Slide 56
Rate? 60 BPM
Regularity? Regular
P waves? Normal
PR interval? 0.36 s
QRS duration? 0.08 s
Interpretation? 1st Degree AV Block

## Slide 57
• Rate? 50 bpm
• Regularity? regularly irregular
P waves? nl, but 4th no QRS
• PR interval? Lengthens
QRS duration? 0.08 s
Interpretation? 2nd Degree AV Block, Type I
(Wenckebach, Mobitz type I)
PR interval progressively lengthens, then the impulse is completely blocked (P wave not followed by QRS)

## Slide 58
• Rate? 40 bpm
• Regularity? Regular
• P waves? nl, 2 of 3 no QRS
• PR interval? 0.14 s
• QRS duration? 0.08 s
Interpretation? 2nd Degree AV Block, Type II
Occasional P waves are completely blocked (P wave not followed by QRS).

## Slide 59
• Rate? 40 bpm
• Regularity? regular
• P waves? no relation to QRS
• PR interval? None
• QRS duration? wide (> 0.12 s)
Interpretation? 3rd Degree AV Block
↑
↑
↑
↑
↑
↑
↑
↑
↑

## Slide 60
Acute Myocardial Infarction

## Slide 61: Diagnosing a MI
To diagnose a myocardial infarction you need to go beyond looking at a rhythm strip and obtain a 12-Lead ECG.
Rhythm Strip
12-Lead ECG

## Slide 62: The 12-Leads
The 12-leads include:
  3 Limb leads (I, II, III)
  3 Augmented leads (aVR, aVL, aVF)
  6 Precordial leads (V1- V6)

## Slide 63: ST Elevation
One way to diagnose an acute MI is to look for elevation of the ST segment.

## Slide 64: ST Elevation (cont)
Elevation of the ST segment (greater than 1 small box) in 2 leads is consistent with a myocardial infarction.

## Slide 65: What part of the heart is affected ?
• II, III, aVF = Inferior Wall
Leads V1, V2, V3, and V4 = Anterior Wall MI
I, aVL, V5 and V6 Lateral wall of left ventricle

## Slide 66: Putting it all Together
Do you think this person is having a myocardial infarction. If so, where?

## Slide 67: Interpretation
Yes, this person is having an acute anterior wall myocardial infarction.

## Slide 68: Putting it all Together
Now, where do you think this person is having a myocardial infarction?

## Slide 69: Inferior Wall MI
This is an inferior MI. Note the ST elevation in leads II, III and aVF.

## Slide 70: Putting it all Together
How about now?

## Slide 71: Anterolateral MI
This person’s MI involves both the anterior wall (V2-V4) and the lateral wall (V5-V6, I, and aVL)!

## Slide 72: Right Bundle Branch Block (RBBB)
Diagnostic criteria for right bundle branch block
  QRS duration >0.12 s
  A secondary R wave (R') in V1 or V2
  Wide slurred S wave in leads I, V5, and V6
Associated feature
  ST segment depression and T wave inversion in the right precordial leads

## Slide 73: Right Bundle Branch Block (RBBB)

## Slide 74: Left Bundle Branch Block (LBBB)
Diagnostic criteria for left bundle branch block
  QRS duration of >0.12 s
  Broad monophasic R wave in leads 1, V5, and V6
  Absence of Q waves in leads V5 and V6
  Associated features
    Displacement of ST segment and T wave in an opposite direction to the dominant deflection of the QRS complex (appropriatediscordance)
    Poor R wave progression in the chest leads
    RS complex, rather than monophasic complex, in leads V5 and V6
    Left axis deviation—common but not invariable finding

## Slide 75: Left Bundle Branch Block (LBBB)

## Slide 83
Q & A
Thanks